## Slide 1: Computer Networks Week2 OSI Model
Presented By
Subhalaxmi Chakraborty

## Slide 2
In 1984, the OSI model was formally adopted by ISO as an international standard
OSI stands for Open Systems Interconnection and consists of 7 Layers
Open Systems Interconnection (OSI) model,
a conceptual framework that describes the functions of a networking or telecommunication system.
In this case, we may need several protocols, for each layer.

## Slide 3
A protocol is a set of rules that govern the data communication .It represents the agreement between two communicating devices.
When communication is not simple, we may divide the complex task of communication into several layers.

## Slide 4: 7 layers of OSI Model

## Slide 5: Interfaces b/w Layers

## Slide 6: OSI in Action
A message begins at the top application layer and moves down the OSI layers to the bottom physical layer.
As the message descends, each successive OSI model layer adds a header to it.
A header is layer-specific information that basically explains what functions the layer carried out.
Conversely, at the receiving end, headers are striped from the message as it travels up the corresponding layers.
OSI Model

## Slide 8: Data Communication using the OSI Model

## Slide 9: Layer7- Application Layer
In the OSI model, this is the layer that is the “closest to the end user”.
Communication at the application layer is between two processes running at the two host.
A web browser (Google Chrome, Firefox, Safari, etc.) or other app - Skype, Outlook, Office - are examples of Layer 7 applications.

## Slide 10
Application layer defines how application processes(clients and servers) are running on different end systems and pass messages to each other.
Protocols of Application layer
HTTP- Hypertext Transfer Protocol
SMTP- Simple Mail Transfer Protocol
FTP- File Transfer Protocol
TELNET- Terminal Network- (for accessing a site remotely)

## Slide 11: Presentation Layer
The presentation layer is an important layer in the OSI model because it is responsible for some of the important services like
Data conversion
Data compression (JPEG)
Data encryption, and decryption (PGP= Pretty Good Privacy), SSL (Secured Socket Layer)

## Slide 12: Session Layer
The session layer establishes a session between the source and the destination nodes , manages and terminates sessions on completion of the communication process.
The protocols used are:
PPTP- Point-to-Point Protocol
SAP-Session Announcement Protocol

## Slide 13: Transport Layer
The transport layer works on two determined communication modes:
Connection oriented and connectionless
This layer transmits data from source to destination node.
It uses the most important protocols of OSI protocol family, which are:
Transmission Control Protocol (TCP)
User Datagram Protocol (UDP)

## Slide 14: TCP vs UDP
TCP is a connection oriented protocol which establishes a connection a logical connection between transport layers at two hosts
TCP provides flow control, error control
TCP allows retransmission of packets
UDP is a connectionless protocol
UDP does not provide flow control, error control
UDP does not allow retransmission of packets

## Slide 15: Network Layer
The network layer is responsible for the delivery of individual packets from the source host to the destination host.
  Logical addressing
  Routing
The network layer assists the following protocols:
Internet Protocol (IPv4)
Internet Protocol (IPv6)
ICMP- Internet Control Message Protocol
It helps IP to report some problems when routing a packet

## Slide 16
End to end delivery of packets
Creates logical paths
Path determination (routing)
Hides the lower layers making things hardware independent
Uses logical hierarchical addresses
Devices: routers

## Slide 17: Different IP classes

## Slide 18: Data link Layer
Devices: switches, bridges, NIC(Network Interface card)
Data link layer has two sub-layers:
Logical Link Control(LLC): It deals with protocols, flow-control, and error control
Media Access Control: It deals with actual control of media

## Slide 19
The data link layer is responsible for moving frames from one hop (node) to the next.
  Framing
  Physical addressing
  Flow control
  Error control
  Access control

## Slide 20: Functionality of Data-link Layer
Framing
Data-link layer takes packets from Network Layer and encapsulates them into Frames. Then, it sends each frame bit-by-bit on the hardware. At receiver’ end, data link layer picks up signals from hardware and assembles them into frames.
-Character oriented framing
-Bit oriented framing

## Slide 21
Addressing
Data-link layer provides layer-2 hardware addressing mechanism. Hardware address /Physical Address/MAC address is assumed to be unique on the link. It is encoded into hardware at the time of manufacturing.
MAC is 6 byte code embedded in NIC.

## Slide 23
Error Control
Sometimes signals may have encountered problem in transition and the bits are flipped. These errors are detected and attempted to recover actual data bits. It also provides error reporting mechanism to the sender.
Flow Control
Stations on same link may have different speed or capacity. Data-link layer ensures flow control that enables both machine to exchange data on same speed.

## Slide 24
Multi-Access
When host on the shared link tries to transfer the data, it has a high probability of collision.
Data-link layer provides mechanism such as CSMA/CD and CSMA/CA to equip capability of accessing a shared media among multiple Systems.
*CSMA/CD- Carrier Sense Multiple Access/ Collision Detection
* CSMA/CA- Carrier Sense Multiple Access/ Collision Avoidance

## Slide 25: Physical Layer
The physical layer is responsible for movements of individual bits from one hop (node) to the next.
  Physical characteristics of interface and medium: pin assignment, connector, cables
  Representation of bits: Linecoding, Modulation
  Data rate- Bit rate, Baud rate
  Synchronization of bits
  Line configuration: point-to-point, multipoint
  Physical topology
  Transmission mode: simplex, half-duplex, full-duplex

## Slide 27
The TCP/IP protocol suite was developed prior to the OSI model.
Therefore, the layers in the TCP/IP protocol suite do not match exactly with those in the OSI model.
Today, however, TCP/IP is thought of as a five-layer model with the layers named similarly to the ones in the OSI model.

## Slide 28
TCP/IP and OSI model

## Slide 29
Q &A
What are the advantages of a multipoint connection over a point-to-point connection?
What is the difference between half-duplex and full-duplex transmission modes?
Name the four basic network topologies, and cite an advantage of each type.
For n devices in a network, what is the number of cable links required for a mesh, ring, bus, and star topology?
What is an internet? What is the Internet?
Why are protocols needed?
What is standard?
In the ring topology in what happens if one of the stations is unplugged?
In the bus topology, what happens if one of the stations is unplugged?
Explain why do we need n(n-1)/2 number of links in mesh topology?